## Slide 1: UART System Design for FPGA

## Slide 2: UART

## Slide 3: UART Transceiver
Serial communication module
Transmitter and Receiver
Transmits one byte at a time
Start bit and a stop bit
One data line for transmitting and another for receiving and no clock: Asynchronous
Default state of the Tx/Rx line is 1
Start bit = 0
Stop bit = 1

## Slide 4
Tx
Rx
Baud rate: Rate at which data is transferred, bits per second
9600 Baud = 9600 bits in one second
PISO
Start bit
Stop bit
data
Clock = 50MHz
Baud rate
Shifting operation should be controlled using an enable signal delayed with respect to baud rate
8 bits
start
stop
1/9600 = 104 us
Generate enable pulse ever 104 us
104 us / 20 ns = 5200 (104 us)
Every 5200 clock cycles of 50 MHz clock, generate one enable pulse. By doing this, 104 us is achieved.

## Slide 5
delayCounter
PISO
bitCounter
FSM
Transmitter

## Slide 6: Assignment
Calculate the number of clock cycles for 1 bit delay to transfer data at 11500 baud rate. Consider 12 Mhz clock
Use the bk_fsm_demo.v. Create a test bench and generate the enable signal with 104 us delay for the design. Consider 50 MHz clock
Come up with the design for UART receiver
  Clue: Use SIPO shift register
2 Hours

## Slide 7
baud_rate_div
Source clock = 50 MHz
T = 20 ns
Required Baud Rate = 9600
9600 cycles should be present per second
50000000/9600 = N = 5208
Baud_rate_div = N/2 = 2604
5208 Cycles of 50 MHz domain T = 104160 ns +- 100
20 ns = One clock cycle
5208 Cycles of 50 MHz domain T = 104160 ns +- 100
always@(posedge source_clock)
if(baud_pulse)
always@(posedge baud_clock)
always@(posedge baud_pulse)
Use as an enable signal in source domain

## Slide 8
Source clock = 50 MHz
T = 20 ns
Required Baud Rate = 9600
9600 cycles should be present per second
50000000/9600 = N = 5208
Baud_rate_div = N/2 = 2604
Source clock = 50 MHz
T = 20 ns
Required Baud Rate = 9600 X 16
153600 cycles should be present per second
50000000/153600 = N = 325
Baud_rate_div = N/2 = 162
1X
16 X

## Slide 9
PISO
Data Path
Control Path

## Slide 10
Sending the start bit and waiting for 16 cycles
Sending the data byte and waiting for 16 cycles every time a bit is transferred
Sending the stop bit and waiting for 16 cycles
Data to send = 1 byte
Start bit = 0
Stop bit = 1
Default = 1
One bit shift

## Slide 11
uart_tx.v
FIFO
FSM
UART Transmitter